# CHAPTER 1
INTRODUCTION
CHAPTER 2
# FLEXIBILITY IN POWER SYSTEMS
For power systems, flexibility can be defined as the ability of the system to maintain the balance between generation and consumption over changing conditions. Variability and uncertainty are important issues for power systems, and to cover the deviations from equilibrium and unexpected situations, enough energy resources are needed. However, the capacity of resources for the flexibility of given power system must be analyzed carefully as providing flexibility is rather expensive.
With the increasing penetration of renewable generations such as wind and solar energies to power systems, energy balance problem becomes harder to achieve, as a consequence of unpredictable and varying nature of renewable sources. Energy storage and demand side management schemes are gaining popularity over the years, which can be combined with renewable energy sources to increase flexibility of power systems.
## Wind Power on Power Systems
With the increasing environmental impacts of electricity production, renewable generation, such as wind and solar energies, has been penetrating to the power systems over the years. Today, 3.7% of global electricity is supplied by wind power and this percentage is expected to increase for the next years [1]. Total installed wind power capacity has reached approximately 487,000 MW at the end of 2016 and is expected to reach around 790,000 MW in 2020 [2]. Installed wind capacity over years can be observed in Figure X [3].

Figure X Historical development of global installed wind capacity
With the increasing penetration of wind energy to power systems, security and reliability of power systems are negatively affected, as a consequence of unpredictable and varying nature of wind. Power output of wind turbine is highly dependent on wind speed and can be expressed as follows:
P = {1} over {2} {ρ} rsub {air} {C} rsub {p} left (λ , β right ) π {r} ^ {2} {v} ^ {3} (X)
where:
Cp(λ,β)	power coefficient, a function of the tip speed ratio λ and the pitch angle β
r	blade length
v	wind velocity
As it can be observed from Equation X, even small variations of wind speed can cause large power fluctuations. In Figure X, fluctuations of power output for a wind farm in Turkey can be observed. Power level frequencies of the wind farm can also be seen in Figure X.

Figure X Generation of a wind farm annually

Figure X Generation levels of a wind farm annually
With the increasing penetration of wind power into power systems, complexity of operation and planning of the systems increases. To cope with unpredictable and variable nature of wind, more power system flexibility is needed for high wind power penetration. To maintain reliability and security of the systems, additional reserves are needed. Energy storage technologies and demand side management schemes can be used for this purpose.
## ENERGY STORAGE SYSTEMS (ESSs)
In a power system, energy demand must be supplied instantaneously to preserve stability and quality of the system. Stability and quality of a power system decreases as an imbalance between supply and demand occurs. Scheduling of power systems with varying net load profile decreases the overall efficiency because of the deviations from optimal generation spot.
With the increasing penetration of renewable energy to power systems, security and reliability issues must be handled carefully, because of unpredictable and inconsistent nature of renewable energy sources. To cope with this problem, ESSs can be used to smooth out variable power generation of renewable energy systems, which makes renewable sources more reliable.
With the help of ESSs, electrical energy can be stored when generation exceeds consumption and stored energy can be used later for compensating generation shortage when needed. By doing this, generation can be maintained at a constant level, which increases the overall efficiency of the system. These systems can also be used for balancing short-term power fluctuations.
Widely-used categorization of ESSs is according to the form of energy used; mechanical, electro-chemical, chemical, electrical and thermal. [4]⁠
- Mechanical
  - Pumped hydro
  - Compressed air
  - Flywheel
- Electro-chemical
  - Secondary batteries
  - Flow batteries
- Chemical
  - Hydrogen
- Electrical
  - Double-layer capacitor
  - Superconducting magnetic coil
- Thermal
  - Sensible heat
  - Latent heat
  - Thermo-chemical
General properties of ESSs can be described as follows:
- Capacity: maximum energy storage limit of the system
- Power: charge/discharge power limit of the system
- Efficiency: ratio of the energy provided by discharging the system to the energy needed to charge the system
- Storage period: duration of stored energy without discharging
- Charge/discharge time: time to charge/discharge the system
- Cost: the capital and operation costs of the system
While choosing the suitable ESSs for a given system, these given properties must be carefully analized. Capacity and power are two important parameters for these systems. Capacity rate can be determined by control and energy management procedures while power rate can be determined by the difference between supply and demand.
Battery Energy Storage Systems (BESSs)
BESSs can be used for compensation of intermittent power output of wind farms. By charging and dicharging BESSs, excess power above predefined threshold levels can be stored and delivered lately. By combining BESSs with wind power generation, throughput of the existing grid infrastructure can be improved. However, it is important to adapt control strategies for optimal use of BESSs, as large-scale utilization of BESSs is not a cost effective choice [5].
BESSs are connected to the system at the point of common coupling and power converters are used for charging/discharging operations of BESSs which is shown in Figure X.
Figure X

Thermal Energy Storage (TES)
Introduction
TES technology is used for storing thermal energy by heating or cooling a storage medium, to be used for heating and cooling needs later. Buildings and industrial processes are the main sectors where TES units are used. With the utilization of TES units, electricity consumption of the buildings does not have to be instantenously with the heating or cooling demand, as heating or cooling demand can be supplied with stored energy, which can be applied to shift electricity consumption. With the effective control of TES units, electric load profile for building’s thermal needs can be rearranged without affecting total energy consumption or temperature comfort for the buildings.
Thermal energy can be stored in three ways, in the form of sensible heat, latent heat or thermo-chemical energy. In the form of sensible heat storage, thermal energy is stored by heating or cooling a liquid or solid storage medium. In the form of latent heat storage, phase change materials (PCMs) are used for storing thermal energy. Thermo-chemical storage (TCS) is based on chemical reactions to store and release thermal energy.
Sensible heat storage is based on the specific heat of a storage medium which limits the storage capacity of these systems. PCMs use latent heat of the phase change and stored energy can be much more higher compared to sensible heat storage. In TCS, thermo-chemical reactions are used to store thermal energy for heating and cooling applications and in these systems storage capacity can be much higher.
Performance of TES units depends on system application and needs. PCM and TCS systems are more expensive compared to sensible heat storage and are suitable for applications where high number of storage cycles are needed.
Chilled water is generated with chillers and cooling towers. Chillers are used for removing the heat from chilled water loop and cooling towers are used for rejecting the heat from chiller cycle to ambient environment.
Storage element is used for shifting cooling thermal energy load. Load shifting logic depends on several factors such as renewable energy penetration, ambient temperature, temperature comfort level.

# CHAPTER 3
MODELLING AND APPROACHES
Modelling of ESSs
In this thesis, ESSs are included to power system with wind power generation. Details of used models for ESSs are explained below.
- BESS
  - Operating Mode
BESS can operate in three modes; charging, discharging and idle. In charging mode, batteries are charged with the power drawn from grid and BESS can be considered as a load. In discharging mode, batteries are discharged and deliver power to the grid and BESS can be considered as a generation unit. In idle mode, batteries are neither charged nor discharged.
  - Energy Equations
Charging efficiency of a BESS is defined as the ratio of rate of change in stored energy in BESS to power drawn from grid in charging mode. Discharging efficiency of a BESS is defined as the ratio of rate of change in stored energy in BESS to power supplied to grid in discharging mode.
SoC of a battery is defined as available capacity of the battery expressed as a percentage of its rated capacity. SOC is an indication of how longer a battery can continue to perform before recharging is needed [6]. Depleting or overcharging a battery is not desired, so proper limitations (i.e., 30%-100%) should be defined for SoC of the battery.
Considering above definitions and limitations, energy equations for BESS model are expressed as;
E^BESS_{t}=E^BESS_{t-1} + (P^{BESS,ch}_t %eta_{BESS,ch} - P^{BESS,dch}_t %eta_{BESS,dch}) %DELTA t (X)
SoC^BESS_{t} = E^BESS_{t} / E^BESS_{max} (X)
SoC^BESS_min < SoC^BESS_{t} < SoC^BESS_max (X)
  - Power Equations
Battery charging and discharging speeds are limited by the physical and chemical characteristics of the BESS. With increasing depth of discharge (DoD), cycle life of a battery decreases and deep discharge can cause permanent damage over battery cells. To protect the battery from a permanent damage and increase the battery cycle life, proper limitation should be set for maximum discharge rating of the battery [7].
Considering above limitations, power equations for BESS model are expressed as;
0 < P^{BESS,ch}_t < P^{BESS,ch}_max (X)
0 < P^{BESS,dch}_t < P^{BESS,dch}_max (X)
- TESS
  - Operating Mode
TESS can operate in three modes; charging, discharging and idle. These modes are explained for cooling and heating applications.
In charging mode, when the output power of chillers/heaters is greater than the power need by buildings, the excess power is stored in TESS. In discharging mode, when the output power of chiller/heater is less than the power need by buildings, TESS compensates for the power difference. In idle mode, TESS is neither charged or discharged.
  - Energy Equations

  - Power Equations
Modelling of Building Temperature
A simplified model for temperature dynamics of a space can be created using a resistance-capacitance (RC) circuit analogy [8],
C dot T = u + P_{d} + ( T_{o} - T ) over R (X)
where
T	inside temperature
Pd	external disturbance load
To	outside temperature
u	heating and cooling power input
The simplified thermal mass model (X) can be used for energy conversion problems, considering entire building and average temperature of all building spaces.
For discrete time, equation (X) can be represented with a sampling time of Δt,
T(k+1) = A T(k) + B u(k) + d(k) (X)
where:
A = 1- {Δt} over {R C} , B = {Δt} over {C} , d = {P_{d} Δt} over {C} + {T_{o} Δt} over {R C}
For the simplification of building model, Pd is ignored and equation (X) becomes,
T_{change} = {Δt} (u over C + {T_{o} - T} over RC) (X)

BESS Capacity
Capacity of a battery is expressed as power and energy capacity [9]. Power capacity of a battery is defined as the supplied or stored power under rated discharge/charge periods, and energy capacity of a battery is defined as the energy that can be stored in and drawn from the battery. Power and energy capacities can be used to determine the capital cost of a BESS [10].
For a system, BESS power can be written as
P_{d}(t) = P_{w}(t)+P_b(t) (x)
where:
Pb(t)	BESS power
Pw(t)	wind power
Pd(t)	dispatched power

CHAPTER 4
SIMULATIONS AND RESULTS
In this thesis, power system computer-aided design (PSCAD)/ electromagnetic transients including dc (EMTDC) is used for the simulations.
CHAPTER 5
CONCLUSIONS AND FUTURE WORK

[1]	“WIND IN NUMBERS | GWEC.” [Online]. Available: http://www.gwec.net/global-figures/wind-in-numbers/. [Accessed: 11-May-2017].
[2]	“Cumulative-Market-Forecast-by-Region-2016-2020-1.jpg (2091×1123).” [Online]. Available: http://www.gwec.net/wp-content/uploads/2016/04/Cumulative-Market-Forecast-by-Region-2016-2020-1.jpg. [Accessed: 11-May-2017].
[3]	“full-text.”
[4]	K. Han and T. Carson, “Executive summary,” Management, vol. II, pp. 10–16, 2008.
[5]	S. Teleke, M. E. Baran, S. Member, S. Bhattacharya, and A. Q. Huang, “Optimal Control of Battery Energy Storage for Wind Farm Dispatching,” IEEE Trans. Energy Convers., vol. 25, no. 3, pp. 787–794, 2010.
[6]	“Battery State of Charge Determination.” [Online]. Available: http://www.mpoweruk.com/soc.htm. [Accessed: 12-May-2017].
[7]	“Battery Life and How To Improve It.” [Online]. Available: http://www.mpoweruk.com/life.htm. [Accessed: 12-May-2017].
[8]	Y. Ma, A. Kelman, A. Daly, and F. Borrelli, “Predictive Control for Energy Efficient Buildings with Thermal Storage: Modeling, Stimulation, and Experiments,” IEEE Control Syst., vol. 32, no. 1, pp. 44–64, 2012.
[9]	A. C. J. N. Baker, “Electrical Energy Storage at the turn of the Millenium,” Power Eng., vol. 13, no. 3, pp. 107–112, 2002.
[10]	T. Lee and N. Chen, “Optimal capacity of the battery energy storage system in a power system,” IEEE Trans. Energy Convers., vol. 8, no. 4, pp. 667–673, 1993.